 Data Sheet / GR-601
u-blox 6
Easy to Use
Ultra-High Performance
GPS Smart Antenna

Version 1.0

The specifications in this document are subject to change without prior notice. NaviSys Technology Corp. assumes no warranties (either expressed or implied) regarding the accuracy and completeness of this document and shall in no event be liable for any loss of profit or any other commercial damage, including but not limited to special, incidental, consequential, or other damages. NaviSys products are not intended for use in medical, life-support devices, commercial aircraft or any applications involving potential risk of personal injury, death, or severe property damage in case of failure of the product.

No part of this document may be reproduced or transmitted in any form by any means without the express written permission of NaviSys Technology Corp.

“NaviSys Technology – Your Location Partner” is a trademark of NaviSys Technology Corp. All brand names and product names used in this document are trademarks or registered trademarks of their respective holders.
Revision History

Ver.	Date	Description
1.0	Dec. 14th, 2011	Initial draft

Contents

# Introduction
## Overview
NaviSys GR-601 is an ultra-high performance, easy to use GPS smart antenna designed with u-blox’s latest 6th generation single chip – G6010ST.
Its high performance enables the quick adoption of AVL, timing, and other location based applications. It supports different electrical interfaces such as USB, RS232, UART TTL etc. The connector interface and cable length could be customized based on MOQ.
The standard NMEA0183 outputs data using datum of WGS-84.
## Main Features
Our experienced design exhibits the full performance of u-blox 6 chip.
- Easy adoption with best performance
- Built-in 25x25x4 (mm) patch antenna
- Built-in backup power for faster position fix. External backup power option is available for high working temperature special application.
- USB/UART TTL/RS232 interface support
- PPS support for timing application
- Compatible with GPSD to support GPS PPS signal over USB
- Fully implementation of ultra-high performance u-blox6 single chip architecture
- High tracking sensitivity of -161 dBm!
- Low power consumption of 56mA for average tracking
- Hardware power saving control pin allowing power on/off GPS via GPIO
- Windows location sensor support
- A-GPS support
## Receiver Specifications
Features	Specifications!
GPS receiver type	50 channels, L1 frequency, C/A code
Horizontal Position Accuracy	< 2.5m (Autonomous) / < 2.0m (WAAS) / (CEP, 50%, 24hr static, -130dBm)
Velocity Accuracy	<0.1 m/s (speed) / <0.5° (heading) / (50%@30m/s)
Accuracy of PPS Signal	30ns (RMS) or <60 ns (99%) / 0.5ms for PPS over USB
TTFF (Time to First Fix) / (50%, -130dBm, autonomous)	Hot Start: 1s / Warm Start: 32s / Cold Start: 32s
Sensitivity / (Autonomous)	Tracking: –161dBm / Acquisition: -147dBm
Measurement data output	Update rate: 1 Hz (default), up to 5 Hz by enabling command / NMEA output protocol: Ver. 2.3 (compatible to 3.0) / UART default baud rate: 9600 bps, (N-8-1) / Datum: WGS-84 / Default: GGA, GLL, GSA, GSV, RMC, VTG, TXT
Max. Altitude	< 50,000 m
Max. Velocity	< 1,852 km/hr
SBAS Support	WAAS, EGNOS, MSAS
Dynamics	< 4g
Power consumption	56mA, continuous tracking mode
Power supply	3.3 ~ 5.5 V
Dimension	36 (W) x 42 (L) x 15 (H) (mm )
Operating temperature	-40°C e. only 30 onsumes only 30 mAiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiiii~ +85°C ( -20~60℃ for backup battery)
Storage temperature	-40°C ~ +85°C ( -40~60℃ for backup battery)

!Note: Data is from chip vendor.
## Protocols
The NMEA protocol is supported via serial UART (RX/TX), RS232 or USB (DM/DP) I/O port. The default supported protocol is NMEA protocol.
1. Serial communication channel – UART/RS232
    1. No parity, 8-data bit, 1-stop bit (N-8-1)
    2. 9600 bps.
2. NMEA 0183 Version 2.3 ASCII output
    1. Default GGA, GSA, GSV, GLL, RMC, VTG and TXT
## PPS Over USB
The GPS PPS signal was born with very high precision 30ns (RMS) or 60ns (99%). Aligning with this signal, time of devices spreading all over the world could be accurately synchronized. GR-601R/GR-601T provides this signal at pin 5.
For the popular USB interface, PPS could be bridged to a USB interface so that USB driver can check this signal for timing. GR-601W is the special USB model designed to deliver PPS signal over USB interface using Prolific PL-2303 USB.
# Hardware Interface
## Dimension

The dimension of GR-601 is 36 mm (W) x 42 mm (L) x 15 mm (H) as shown above.
## I/O Connectors and Pin Assignment
	GR-601T	GR-601R	GR-601U/W
	2 / 1 / 3 / 4 / 5 / 6	2 / 1 / 3 / 4 / 5 / 6
Pin	Mini-Din 6-pin PS/2 Male Plug	Mini-Din 6-pin PS/2 Male Plug	USB A type / Male Plug
1	GND	GND	VDD 5V
2	VCC	VCC	D-
3	TXD-TTL	TX-RS232	D+
4	RXD-TTL	RX-RS232	GND
5	PPS	$PPS	-
6	PWR_CTRL	PWR_CTRL	-

$: RS232 signal level for longer distance transmission
Pin	Name	Function	I/O
1	GND/VDD	Ground / USB 5 VDC power supply	Input
2	VCC/D-	Power supply (3.3 ~ 5.5 VDC) / USB D-	Input / IO
3	TX/D+	Serial data output (from GPS) / USB D+	Output / IO
4	RX/GND	Serial data input (into GPS) / USB ground	Input
5	PPS	PPS signal for precise GPS time synchronization	Output
6	PWR_CTRL	Power control; High/floating: ON, Low: OFF	Input

Power Saving
GR-601 supports the hardware power saving mechanism. To control the power of GR-601, connect the PWR_CTRL pin to a GPIO of a micro-processor. To cut off the power of GR-601 (VCC is always connected to power source), just pull the PWR_CTRL pin low (in this case, GR-601 only keeps power of RTC and RAM). During normal run, pull it high or leave it floating (in this case, GR-601 is fully powered).
## Cable Length, Dimension and LED
The default cable length for different models is shown below.

Cable Length	1.5m for GR-601U / 3m for GR-601R / <1m for GR-601T

An embedded LED is used to indicate the GPS position fixing status as following:
LED always ON: Position is not fixed, under fixing
LED Blinking: Position is fixed

Note.
Customization options: cable length (0.1~15m), connector type (DB9/25, RJ11/45, MicroFit, SM-4Y etc), higher voltage input (12/24V etc).
# Software Interface
## NMEA Output Messages
The NMEA-0183 Output Messages are shown as below:
NMEA Record	Descriptions
GPGGA	Global positioning system fixed data: time, position, fixed type
GPGLL	Geographic position: latitude, longitude, UTC time of position fix and status
GPGSA	GPS receiver operating mode, active satellites, and DOP values
GPGSV	GNSS satellites in view: ID number, elevation, azimuth, and SNR values
GPRMC	Recommended minimum specific GNSS data: time, date, position, course, speed
GPVTG	Course over ground and ground speed
GPTXT	u-blox message

The GR-601 adopts interface protocol of National Marine Electronics Association's NMEA-0183 Version 2.3 interface specification. GR-601 supports 7 types of NMEA sentences (GPGGA, GPGLL, GPGSA, GPGSV, GPRMC, GPVTG, and GPTXT).
The default output sentences are GPGGA, GPGSA, GPGSV, GPRMC, GPVTG and GPGLL. The default UART communication parameters are 9600 bps, 8 data bits, 1 stop bit, and no parity.
Message examples:
$GPRMC,065500.00,A,2447.65027,N,12100.78318,E,15.869,189.32,051109,,,D*57
$GPVTG,189.32,T,,M,15.869,N,29.405,K,D*30
$GPGGA,065500.00,2447.65027,N,12100.78318,E,2,12,0.91,69.8,M,16.3,M,,*65
$GPGSA,A,3,20,02,23,13,50,42,04,11,17,28,32,08,1.53,0.91,1.22*0D
$GPGSV,4,1,13,02,10,252,26,04,39,268,40,08,09,197,41,11,17,058,32*7B
$GPGSV,4,2,13,13,06,144,23,17,50,345,43,20,45,056,44,23,11,109,37*72
$GPGSV,4,3,13,27,02,301,,28,73,194,39,32,20,043,38,42,54,140,34*7B
$GPGSV,4,4,13,50,51,133,33*4B
$GPGLL,2447.65027,N,12100.78318,E,065500.00,A,D*6E
$GPTXT,01,01,02,u-blox ag - www.u-blox.com*50
## GPGGA - Global Positioning System Fix Data
- Example $GPGGA,065500.00,2447.65027,N,12100.78318,E,2,12,0.91,69.8,M,16.3,M,,*65
- Explanation
Contents	Example	Unit	Explanation
Message ID	$GPGGA		GGA protocol header
UTC Time	065500.00		hhmmss.ss / hh: hour, mm: minute, ss: second
Latitude	2447.65027		ddmm.mmmmm / dd: degree, mm.mmmmm: minute
North/South	N		N: North Latitude, S: South Latitude
Longitude	12100.78318		dddmm.mmmmm / dd: degree, mm.mmmmm: minute
East/West	E		E: East Longitude, W: West Longitude
Position Fix Indicator	2		0: Fix not available or invalid, / 1: GPS SPS Mode, fix valid, / 2: Differential GPS, SPS Mode, fix valid, / 3~5: Not supported, / 6: Dead Reckoning Mode, fix valid
Satellites Used	12		Number of satellites used in positioning calculation (0 to 12)
HDOP	0.91		Horizontal Dilution of Precision
MSL Altitude	69.8	meters
Unit	M		Meters
Geoidal separation	16.3	meters
Units	M		Meters
Age of Diff. Corr.		second	Null fields when DGPS is not used
Diff. Ref. Station ID
checksum	*65
<CR><LF>			End of sentence

## GPGLL - Geographic Position - Latitude / Longitude
Example
$GPGLL,2447.65027,N,12100.78318,E,065500.00,A,D*6E
Explanation
Contents	Example	Unit	Explanation
Message ID	$GPGLL		GLL protocol header
Latitude	2447.65027		ddmm.mmmmm / dd: degree, mm.mmmmm: minute
North/South	N		N: North Latitude, S: South Latitude
Longitude	12100.78318		dddmm.mmmmm / dd: degree, mm.mmmmm: minute
East/West	E		E: East Longitude, W: West Longitude
UTC Time	065500.00		hhmmss.ss / hh: hour, mm: minute, ss: second
Status	A		A: Data valid, V: Data invalid
Mode Indicator	D		A: Autonomous, D: DGPS, E: DR
checksum	*6E
<CR><LF>			End of sentence

## GPGSA - GNSS DOP and Active Satellites
Example
$GPGSA,A,3,20,02,23,13,50,42,04,11,17,28,32,08,1.53,0.91,1.22*0D
Explanation
Contents	Example	Explanation
Message ID	$GPGSA	GSA protocol header
Mode 1	A	M: Manual—forced to operate in 2D or 3D mode / A: 2D Automatic—allowed to automatically switch 2D/3D
Mode 2	3	1: Fix not available / 2: 2D (<= 4 Satellites used) / 3: 3D (>= 4 Satellites used)
Satellite used in solution	20	Satellite on Channel 1
Satellite used in solution	02	Satellite on Channel 2
…		Display of quantity used (12 max) / If less than 12 SVs are used for navigation, the remaining fields are left empty. If more than 12 SVs are used for navigation, only the IDs of the first 12 are output.
PDOP	1.53	Position Dilution of Precision
HDOP	0.91	Horizontal Dilution of Precision
VDOP	1.22	Vertical Dilution of Precision
checksum	*0D
<CR><LF>		End of sentence

## GPGSV - GNSS Satellites in View
Example
$GPGSV,4,1,13,02,10,252,26,04,39,268,40,08,09,197,41,11,17,058,32*7B
$GPGSV,4,2,13,13,06,144,23,17,50,345,43,20,45,056,44,23,11,109,37*72
$GPGSV,4,3,13,27,02,301,,28,73,194,39,32,20,043,38,42,54,140,34*7B
$GPGSV,4,4,13,50,51,133,33*4B
Explanation
Contents	Example	Unit	Explanation
Message ID	$GPGSV		GSV protocol header
Number of messages	4		Range 1 to 4
Message number	1		Range 1 to 4
Satellites in view	13		Number of satellites visible from receiver
Satellite ID number	02		Channel 2 (Range 1 to 64) / The satellite ID numbers are in the range of 1 to 32 for GPS satellites, and 33 to 64 for SBAS satellites (ID=120-PRN; e.g. SV ID 33 is SBAS PRN 120, 34 is SBAS PRN 121, and so on)
Elevation	10	degrees	Elevation angle of satellite as seen from receiver channel 1 (00 to 90)
Azimuth	252	degrees	Satellite azimuth as seen from receiver channel 1 (000 to 359)
SNR (C/No)	26	dBHz	Received signal level C/No from receiver channel 1 (00 to 99, null when not tracking)
…
Satellite ID number	11		Channel 4 (Range 1 to 32)
Elevation	17	degrees	Elevation angle of satellite as seen from receiver channel 4 (00 to 90)
Azimuth	058	degrees	Satellite azimuth as seen from receiver channel 4 (000 to 359)
SNR (C/No)	32	dBHz	Received signal level C/No from receiver channel 4 (00 to 99, null when not tracking)
checksum	*71
<CR><LF>			End of sentence

## GPRMC - Recommended Minimum Specific GNSS Data
Example
$GPRMC,065500.00,A,2447.65027,N,12100.78318,E,15.869,189.32,051109,,,D*57
Explanation
Contents	Example	Unit	Explanation
Message ID	$GPRMC		RMC protocol header
UTC Time	065500.00		hhmmss.ss / hh: hour, mm: minute, ss: second
Status	A		A: Data valid, V: Data invalid
Latitude	2447.65027		ddmm.mmmmm / dd: degree, mm.mmmmm: minute
North/South	N		N: North Latitude, S: South Latitude
Longitude	12100.78318		dddmm.mmmmm / dd: degree, mm.mmmmm: minute
East/West	E		E: East Longitude, W: West Longitude
Speed over ground	15.869	knots	Receiver’s speed
Course over ground	189.32	degrees	Receiver’s direction of travel / Moving clockwise starting at due north
Date	051109		ddmmyy / dd: Day, mm: Month, yy: Year
Magnetic variation		degrees	This receiver does not support magnetic declination. All “course over ground” data are geodetic WGS84 directions.

Mode Indicator	D		A: Autonomous M: Manual / D: DGPS S: Simulation / E: Dead Reckoning N: Data Invalid
checksum	*57
<CR><LF>			End of sentence

## GPVTG - Course over Ground and Ground Speed
Example
$GPVTG,189.32,T,,M,15.869,N,29.405,K,D*30
Explanation
Contents	Example	Unit	Explanation
Message ID	$GPVTG		VTG protocol header
Course over ground	189.32	degrees	Receiver’s direction of travel / Moving clockwise starting at due north (geodetic WGS84 directions)
Reference	T		True
Course over ground		degrees	Receiver’s direction of travel
Reference	M		Magnetic
Speed over ground	15.869	knots	Measured horizontal speed
Unit	N		Knots
Speed over ground	29.405	km/hr	Measured horizontal speed
Unit	K		km/hr
Mode Indicator	D		A: Autonomous, D: DGPS, E: DR
checksum	*30
<CR><LF>			End of sentence

# Evaluation Information
## Overview
Suggest connecting GR-601 to PC and checking its performance using GPS viewer tool. One can download the Navisys GPS viewer tool for u-blox from web site as shown in next section.

## USB Drivers
USB drivers are available from Navisys download link as shown below: http://www.navisys.com.tw/support/download01.htm

Click on Download and it prompts for ID and password. Enter ID and Password and then click on Sign In to download the drivers. The default password is “navi-utility”. Navisys may change the ID and password.

## Ordering Information
GR-601X
T	TTL; mini-din 6-pin male connector
R	RS232; mini-din 6-pin male connector
U	u-blox USB; type A connector
W	Prolific USB, PPS connected to DCD; type A connector

## Related Document
[1] u-blox 6 Receiver Description Including Protocol Specification
http://www.u-blox.com/images/downloads/Product_Docs/u-blox6_ReceiverDescriptionProtocolSpec_%28GPS.G6-SW-10018%29.pdf
# Electrical and Environmental Data
Electrical Data
Power Supply (VDC)	3.3 ~ 5.5
Power Consumption / (w/o antenna)	56mA/average tracking
Backup power	1.4 ~ 3.6 V
USB I/O (V)	VIH: 2.0 ~ VDD_USB (VDD_USB: 3.3V) / VIL: 0 ~ 0.8 / VOH >= 2.8 / VOL<= 0.3
Digital I/O (V)	VIH: 0.7*VDD_IO ~ VDD_IO (VDD_IO: 3.3V) / VIL 0 ~ 0.2*VDD_IO / VOH >= VDD_IO-0.4V / VOL<= 0.4
Protocols	NMEA (default)

Environmental Data
Operating temperature	-40 ~ 85℃ ( -20~60℃ for backup battery)
Storage temperature	-40 ~ 85℃ ( -40~60℃ for backup battery)
Vibration	5Hz to 500Hz, 5g
Shock	Half sine 30g/11ms
RoHS compliant	Yes